Nicholas Smith
CS 485
Project 4
5/4/15
This assignment uses the calibrateCamera function in OpenCV. This function maps vectors of world coordinates to vectors of image coordinates. It computes the rotation vectors, translation vectors, distance coefficients, and intrinsic parameters of the camera. OpenCV also has a projectPoints function that takes the parameters from calibrateCamera and projects the world coordinates provided as input to the image coordinates.
Image Number	Average Projection Error (in pixels)
1	0.2898
2	0.2741
3	0.2732
4	0.2490
5	0.2670
6	0.2912
7	0.2832
8	0.287
9	0.3209
10	0.2947
11	0.3278
12	0.3143
13	0.3521
14	0.2777
15	0.2599
All Images	0.2908

The average projection error for all of the images shows that the parameters are correct up to approximately 0.3 pixels. Some images have a low error of 0.2490 pixels and a high error of 0.3521 pixels with a standard deviation of 0.0267 pixels. These results are good because they are accurate to about 1 pixel.